CmdHPSDRProgrammer is a cross platform command command line program with most the functionality of the HPSDRProgrammer but as a command line program. It can be used to:
- Detecting the network connected to your computer
- Detecting HPSDR board(s) on one of your networks
- Changing the IPv4 address of your HPSDR board.
- Or specifying the address to come from DHCP
- Erasing and Programming firmware into the FPGA of your HPSDR Board by talking with the previous firmware.

The program will run on Linux, MacOS and Windows and can run on amd64, 386, arm architectures.

I did most of the development on the Linux 64 platform so that is the most thoroughly tested platform.

I will demonstrate the use of the program and describe platform differences we will start with Linux.

At the command prompt represented here as the “$” we type the name of the program in the directory where you put the executable file. Note that on Linux you need to put the path to the program using “./” to indicate the current working directory.
To start we just type the program name.

$./CmdHPSDRProgrammer
CmdHPSDRProgrammer version:(0.1.0)
    By Dave KV0S, 2014-11-24, GPL2
    Last Updated: 2015-1-24

    For a list of commands use -help

Interfaces on this Computer:
    lo ()
    eth0 (00:60:97:98:72:c2)
    eth1 (00:1f:c6:7e:52:de)

Here we get the name of the program the version the author and the license, and the date of last update. There is a reminder the -help provides a help screen.

It also lists the interfaces on this computer.
 In this case we have lo which is a loopback, eth0 which is ethernet 0 and eth1 which erthernet 1.

If we type the command with the -help switch we get the following.

$./CmdHPSDRProgrammer --help
Usage of ./CmdHPSDRProgrammer:
  -ddelay=2: Discovery delay before a rediscovery
  -debug="none": Turn debugging and output type, (none, dec, hex)
  -interface="none": Select one interface
  -load="none": Load a saved command file from default or a named file
  -save="none": Save these current flags for future use in default or a named file
  -selectMAC="none": Select Board by MAC address
  -setIP="none": Set IP address, unused number from your subnet or 0.0.0.0 for DHCP
  -setRBF="none": Select the RBF file to write to the board
  -settings="none": Show the settings values (show)

This lists the available switches their default values and a description of the the switch will do.

Because on some machine the setting of these switched are long, There also is a mechanism to sane the users switch settings. The follow is how to see the current saved settings. If no setting have been saved these will be set to the default values.

$./CmdHPSDRProgrammer -settings=show
    Saved Settings:
        Interface: none
        Filename: none
      Selected MAC: (none)
        SetRBF: none
        Debug: none
        Ddelay: 2

     Temp settings:
        Settings: show
        SetIP: none
        Save: none
        Load: none

    lo ()
    eth0 (00:60:97:98:72:c2)
    eth1 (00:1f:c6:7e:52:de)

You can use saved setting for some items and command line settings for other items. The save settings are read first then the current command line.

If you select an interface the program will list some useful information about the computer you are using and list all HPSDR boards found on the selected interface.

$./CmdHPSDRProgrammer -interface=eth1
        Computer: (00:1f:c6:7e:52:de)
        OS: linux (amd64) 4 CPU(s)
        IPV4: 192.168.1.10
        IPV6: fe80::21f:c6ff:fe7e:52de

       HPSDR Board: (0:4:a3:d3:a1:94)
        IPV4: 192.168.1.22
        Port: 1024
        Type: Metis
        Firmware: 2.9
        Status: not running

       HPSDR Board: (0:4:a3:64:25:95)
        IPV4: 192.168.1.27
        Port: 1024
        Type: Hermes
        Firmware: 3.0
        Status: not running

Note one of the items it to tells you if the board on the interface is currently in use on the current interface. Note the Hermes listed here is in use.

$./CmdHPSDRProgrammer -interface=eth1
        Computer: (00:1f:c6:7e:52:de)
        OS: linux (amd64) 4 CPU(s)
        IPV4: 192.168.1.10
        IPV6: fe80::21f:c6ff:fe7e:52de

       HPSDR Board: (0:4:a3:d3:a1:94)
        IPV4: 192.168.1.22
        Port: 1024
        Type: Metis
        Firmware: 2.9
        Status: not running

       HPSDR Board: (0:4:a3:64:25:95)
        IPV4: 192.168.1.28
        Port: 1024
        Type: Hermes
        Firmware: 3.1
        Status: running
To select the board you want to perform specific actions on you use the -selectMAC switch with the value of the boards MAC address. Note while the iout put include the parentheses they are not included in the switch statement.

$./CmdHPSDRProgrammer -interface=eth1 -selectMAC=0:4:a3:64:25:95
        Computer: (00:1f:c6:7e:52:de)
        OS: linux (amd64) 4 CPU(s)
        IPV4: 192.168.1.10
        IPV6: fe80::21f:c6ff:fe7e:52de

      Selected MAC: (0:4:a3:64:25:95)
       HPSDR Board: (0:4:a3:64:25:95)
        IPV4: 192.168.1.27
        Port: 1024
        Type: Hermes
        Firmware: 3.0
        Status: not running

Now that we have a selected board we can change the IP address. Please check you router for address that are in use as the Programmer will change to any valid address in the subnet. It does guard against a few protected addresses and will warn if you are changing subnets.

The following command change the IPv4 address from 192.168.1.27 to 192.168.1.28 and then performs a rediscovery to show the new address is working as in this example.

 $./CmdHPSDRProgrammer -interface=eth1 -selectMAC=0:4:a3:64:25:95 -setIP=192.168.1.28
        Computer: (00:1f:c6:7e:52:de)
        OS: linux (amd64) 4 CPU(s)
        IPV4: 192.168.1.10
        IPV6: fe80::21f:c6ff:fe7e:52de

      Selected MAC: (0:4:a3:64:25:95)
     Changing IP address from 192.168.1.27 to 192.168.1.28

       HPSDR Board: (0:4:a3:64:25:95)
        IPV4: 192.168.1.28
        Port: 1024
        Type: Hermes
        Firmware: 3.1
        Status: not running

The CmdHPSDRProgrammer can change the firmware if the old firmware is UDP enabled. Here is an example of updating the firmware on the Hermes board.

 $./CmdHPSDRProgrammer -interface=eth1 -selectMAC=0:4:a3:64:25:95 -setRBF=/home/hpsdr/Downloads/Hermes_V3.1.rbf
        Computer: (00:1f:c6:7e:52:de)
        OS: linux (amd64) 4 CPU(s)
        IPV4: 192.168.1.10
        IPV6: fe80::21f:c6ff:fe7e:52de

      Selected MAC: (0:4:a3:64:25:95)

      Erasing the HPSDR Board
        Seconds: 12
      Erasing Done

    Found rbf file: /home/dlarsen/Downloads/Hermes_V3.1.rbf
     Size rbf file: 646967
Size rbf in memory: 647168
        Packets: 2528

        Percent: 100

       HPSDR Board: (0:4:a3:64:25:95)
        IPV4: 192.168.1.28
        Port: 1024
        Type: Hermes
        Firmware: 3.1
        Status: not running

This would be the normal interface for regular updating of the firmware.

If for some reason you are having problems there is a debug switch with two output versions.
The first is decimal mode as shown here.

$./CmdHPSDRProgrammer -interface=eth1 -debug=dec
Discover
sent : 255.255.255.255:1024: [239 254 2 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0] : length=64

received : 192.168.1.28:1024: [239 254 2 0 4 163 100 37 149 31 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0] : length=64

received : 192.168.1.22:1024: [239 254 2 0 4 163 211 161 148 29 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0] : length=64

The debug output shows the entire packet the address sent and the packet size. It also shows the packets received back from the boards.

The other mode is hex mode as shown here. Both example are the board discovery.

$./CmdHPSDRProgrammer -interface=eth1 -debug=hex
Discovery
sent : 255.255.255.255:1024: effe0200000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

received : 192.168.1.28:1024: effe020004a36425951f010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010100000000 : length=64

received : 192.168.1.22:1024: effe020004a3d3a1941d000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

As I pointed out previously the command line switches can be view by using the -setting switch. Here is an example with its output.

 $./CmdHPSDRProgrammer -interface=eth1 -debug=hex -settings=show
    Saved Settings:
        Interface: eth1
        Filename: none
      Selected MAC: (none)
        SetRBF: none
        Debug: hex
        Ddelay: 2

     Temp settings:
        Settings: show
        SetIP: none
        Save: none
        Load: none

Discovery
sent : 255.255.255.255:1024: effe0200000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

received : 192.168.1.22:1024: effe020004a3d3a1941d000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

received : 192.168.1.28:1024: effe020004a36425951f010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010100000000 : length=64

We can save these switch settings for reuse in repetitive tasks. The most common method is -save=default this will save to a file CmdHPSDRProgrammer.json file in the current working directory. Here is a example saving the interface and debug settings.

./CmdHPSDRProgrammer -interface=eth1 -debug=hex -save=default
Discovery
sent : 255.255.255.255:1024: effe0200000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

received : 192.168.1.22:1024: effe020004a3d3a1941d000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

received : 192.168.1.28:1024: effe020004a36425951f010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010100000000 : length=64

Now we can the following command and note that interface and debug use the values in the default file.

$./CmdHPSDRProgrammer -load=default -settings=show
    Saved Settings:
        Interface: eth1
        Filename: CmdHPSDRProgrammer.json
      Selected MAC: (none)
        SetRBF: none
        Debug: hex
        Ddelay: 2

     Temp settings:
        Settings: show
        SetIP: none
        Save: none
        Load: default

Discovery
sent : 255.255.255.255:1024: effe0200000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

received : 192.168.1.22:1024: effe020004a3d3a1941d000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

received : 192.168.1.28:1024: effe020004a36425951f010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010100000000 : length=64

If you want to save several different settings files the program will accept the following input where the settings are saved to the file “mymetis.json”.

$./CmdHPSDRProgrammer -interface=eth1 -debug=hex -save=mymetis.json
Discovery
sent : 255.255.255.255:1024: effe0200000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

received : 192.168.1.28:1024: effe020004a36425951f010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010100000000 : length=64

received : 192.168.1.22:1024: effe020004a3d3a1941d000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

And this is a example of load the mymetis.json file. Note that only some the the setting can be saved the temp settings can not be save to avoid mistakenly changing or programming your board.

$./CmdHPSDRProgrammer -debug=hex -load=mymetis.json -settings=show
    Saved Settings:
        Interface: eth1
        Filename: mymetis.json
      Selected MAC: (none)
        SetRBF: none
        Debug: hex
        Ddelay: 2

     Temp settings:
        Settings: show
        SetIP: none
        Save: none
        Load: mymetis.json

Discovery
sent : 255.255.255.255:1024: effe0200000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

received : 192.168.1.28:1024: effe020004a36425951f010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010101010100000000 : length=64

received : 192.168.1.22:1024: effe020004a3d3a1941d000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000 : length=64

All the setting files are plain text so you can use a text editor to change the settings as well. Here is the mymetis.json file.

$cat mymetis.json
{
"Filename": "mymetis.json",
"Intface": "eth1",
"SelectMAC": "none",
"SetRBF": "none",
"Debug": "hex",
"Ddelay": 2
}